## Slide 1
Liquid Neural Network–Based Imputation of Missing Groundwater Time Series Under Sparse Observations
Henok Teklu¹, Norman L. Jones¹, Gustavious P. Williams¹
¹Brigham Young University · Department of Civil & Construction Engineering
1
The Problem
Groundwater monitoring wells are the primary source of water-table elevation (WTE) data, yet public databases worldwide suffer from temporal gaps spanning months to years.
2
Matrix Completion
Wells share patterns — seasonal cycles, drought responses, recharge trends — so the well × time matrix is approximately low-rank. Iterative SVD (SoftImpute) simultaneously recovers missing entries from observed entries across wells.
Target well observed values + gaps
15 donor wells top-correlated, Pearson-weighted
5 GLDAS rows monthly + 1/3/5/10-yr rolling avgs
sin / cos 12-mo seasonal encoding
Target well
to be imputed
15 donor wells
Pearson-weighted neighbors
5 GLDAS aux. rows
monthly + 1/3/5/10-yr avgs
sin / cos seasonal
12-month period
Target obs.
well measurements
Gap
to impute
Donor wells
spatial context
GLDAS aux.
climate anchor
Seasonal
sin / cos cycle
3
Liquid Neural Network
A Closed-form Continuous-time (CFC) Liquid Neural Network (Hasani et al., 2022) models the hidden state as a continuous flow, solved analytically at each step — no numerical ODE solver required. The leak rate λ sets memory horizon. Inputs concatenate MC output, GLDAS soil moisture, and seasonal encoding. The ridge readout is trained ONLY on observed values — MC drives the reservoir through gap periods.
Input vector u(t)
MC output
spatial context
GLDAS
soil moisture
sin / cos
seasonality
Reservoir state x(t)
closed-form continuous-time state
Model output — continuous
Ridge readout
trained ONLY on observed values
AUTO-TUNED PER WELL
TRIALS
8
RESERVOIR
10–80
LEAK RATE
0.05–0.95
ENSEMBLE
3 seeds
OBJECTIVE
KGE
each well's hyperparameters optimized independently via Optuna
4
How GLDAS Anchors the Model
GLDAS is NASA satellite-derived soil moisture. We treat its five channels — one raw monthly plus four rolling averages (1, 3, 5, 10 years) — as parallel timescale strata. Every stratum reports every month: the SVD taps them whenever a well falls silent.
5 AUXILIARY CHANNELS
soilw
raw monthly
soilw_yr01
1-year avg
soilw_yr03
3-year avg
soilw_yr05
5-year avg
soilw_yr10
10-year avg
5
The Combined Pipeline
STAGE 1 · PCHIP
Shape-preserving interpolation for short gaps. Densifies the network for better donor correlations.
STAGE 2 · Matrix Completion
ARCHI selects the top-15 donors. SoftImpute on composite matrix with adaptive SVD rank (3–12).
STAGE 3 · LNN Refinement
Continuous-time CFC dynamics. MC output drives the reservoir; readout trained on real observations only.
Design principle
MC supplies spatial context (what do nearby wells say?). LNN supplies temporal dynamics (how does the system evolve between observations?). Neither alone delivers what the coupled framework does.
6
Cross-Validation Results
592 wells · Great Salt Lake Basin · 2000–2023
0.85
KGE @ 50% removed
50 trials per missing-rate level
0.82
KGE @ 5-yr gap
20 trials per gap-length level
Random missing data (50 trials / level)
% Removed | KGE | R² | RMSE (ft)
5% | 0.837 | 0.771 | 2.53
20% | 0.853 | 0.787 | 2.64
30% | 0.844 | 0.770 | 2.79
50% | 0.847 | 0.788 | 2.74
Consecutive-year gaps (20 trials / level)
Gap length | KGE | R² | RMSE (ft)
1 year | 0.783 | 0.703 | 2.98
3 years | 0.802 | 0.730 | 3.02
5 years | 0.815 | 0.744 | 2.91
7
Conclusions & Applicability
①
First hybrid MC+LNN framework for groundwater: MC for cross-well correlations, LNN for continuous-time dynamics on climate auxiliaries.
②
KGE > 0.84 (random ≤50%) and KGE > 0.78 (gaps ≤5 yr) — substantially exceeding prior ELM methods (beyond 2-yr gaps).
③
PCHIP densification lifts the full pipeline by 10–19% KGE via stronger donor correlations.
④
Plug-and-play: needs only incomplete well records + public GLDAS. No calibration.
ACKNOWLEDGMENTS
Funding for this project was provided by the National Oceanic and Atmospheric Administration (NOAA), awarded to the Cooperative Institute for Research on Hydrology (CIROH) through the NOAA Cooperative Agreement with The University of Alabama. Grant number: A24-0421-S001.
CORRESPONDING AUTHOR
Henok Teklu
anom37@byu.edu
Brigham Young University